## Slide 1: Rotating Machines diagnosis with Time-Frequency Analysis: Focus on Helicopter Gearboxes
Anas Had
LASPI UJM - Saint Etienne
10 November 2023

## Slide 2: About me
Full Name : HAD Anas
Lecturer and researcher at the Sciences and technologies Faculty – UJM (Since 2021)
Laboratory : LASPI – IUT de Roanne.
Research domain : Signal processing – Rotating Machine diagnosis / health monitoring – Biomedical signal processing – Sparsity

## Slide 3: Context – Problem – Objectives
Machine health monitoring
Das, O., Das, D. B., & Birant, D. (2023). Machine learning for fault analysis in rotating machinery: A comprehensive review. Heliyon.
Why Monitor rotating machines?
Rotating Machines are an indispensable element in the industry
They need to be functional all time for production in good conditions
Prevent a catastrophic failure can lead to expensive repairs and hurt the operators
Measurement : Vibration data, Tachometer data, Acoustic…
Objective :
  Early detection of a mechanical component degradation.
  Accurate tracking of the fault progression.

## Slide 4: Context – Problem – Objectives
Most of the proposed rotating machines diagnostic techniques assume the stationarity of the signals.
Problem definition
Constraints :
- From time-frequency maps to scalar indicators.
- Robust for different functioning conditions.
- Detect at first sight.
Solution: Time-Frequency Representations !!
Problem: How to overcome the time varying conditions for the detection of rotating machines faults?

## Slide 5: Helicopter Gearboxes
Why planetary gearbox ?
Compact design with high torque multiplication ratio
They allow for load sharing among multiple gears, which can enhance durability and efficiency.
Epicyclic Gearbox
URL : https://www.youtube.com/watch?v=0ZbTN6pM2SE

## Slide 6: Planetary gears anisotropy detection
Aim : Use vibration data to detect planet gears anisotropy in a helicopter main gearbox.
Key idea : The presence of a planet gear anisotropy is highlighted by the presence of the same time-frequency patterns across multiple adjacent signals.
The proposed general approach :
General approach (Proposed by Airbus Helicopters)
Accelerometer sensor
Computation of two time-frequency fault map for two adjacent signals.
Computation of similarity indicator between two adjacent maps.

## Slide 7: Time-frequency fault map
Vibration signal in time domain
Tachometer Signal
Resampling in angular domain
Time synchronous Averaging
STFT for each carrier revolution
Compute the variance of STFT maps
1. Estimate the correspondence between the time domain and the angular domain.
2. Estimate the angular signal through interpolation.
The angular resampling approach

## Slide 8: Time-frequency fault map
Vibration signal in time domain
Tachometer Signal
Resampling in angular domain
Time synchronous Averaging
STFT for each carrier revolution
Compute the variance of STFT maps
Time synchronous Averaging
Cycle : Planet/ring hunting-tooth averaged signals /
Benefits : Reduce the non-synchronous components and noise by .
Ha, J. M., Youn, B. D., Oh, H., Han, B., Jung, Y., & Park, J. (2016). Autocorrelation-based time synchronous averaging for condition monitoring of planetary gearboxes in wind turbines. Mechanical Systems and Signal Processing, 70, 161-175.

## Slide 9: Time-frequency fault map
Short-Time Fourier Transform
Tradeoff : Time resolution Vs frequency resolution.
Vibration signal in time domain
Tachometer Signal
Resampling in angular domain
Time synchronous Averaging
STFT for each carrier revolution
Compute the variance of STFT maps

## Slide 10: Time-frequency fault map
Short-Time Fourier Transform
Vibration signal in time domain
Tachometer Signal
Resampling in angular domain
Time synchronous Averaging
STFT for each carrier revolution
Compute the variance of STFT maps
Objectif : The variance of the STFT maps highlights the regions where the variability is maximum due to a different planet passing close to the sensor.

## Slide 11: The linearization of time-frequency fault map
The linearization method
Determine the highest points in the map
Create a new class and select a reference point (max)
Assign nearby points the same class as the reference point
More nearby points ?
Define the previous points as reference points.
All the points are assigned to a class?
Yes
No
No
End
Yes

## Slide 12: The proposed indicator
Steps
S2
S3
S1
Spot at
Spot at
For two adjacent binarized maps :
Compute the intersection between the two surfaces
Compute the symmetric difference
Compute :
  If : Spot moves or deforms → no anisotropy.
  If : Spot is fixed → presence of anisotropy.
Compute the indicator :

## Slide 13: The problem with the proposed map
Problems :
Presence of several black spots in TF map.
The black spot divide the energetic spots into two.
Performance degradation du the black spots.
Cause :
Variance of STFTs maps Similar to the spectrogram
The STFT parameters :
  The window and its length Spectral content overlapping
Other causes ?
Black holes

## Slide 14: The problem with the proposed map
Let’s consider where :
is periodic with the carrier revolution
is the contribution of the anisotropic planet gear
The STFT is a linear transformation :
The variance with respect to the carrier revolution :
The variance of the STFT maps suffers from the same problems as the spectrogram Interferences due to the quadratic superposition.
Variance of STFT maps

## Slide 15: The problem with the proposed map
Solutions :
Chose another Time-Frequency Representation with better TF resolution:
  Use a TFR from the Cohen class to attenuate interferences
Reduce the interference by reducing the number of components in signal:
  Filtering around the frequencies of interest
Improvement :
Reduce the resonance phenomena :
  Spectral whitening
Focus on a region of interest :
  Use the Zoom-fft technique to accelerate the TF maps computation.
Black holes

## Slide 16: Improved time-frequency map
Vibration signal in time domain
Tachometer Signal
Resampling in angular domain
Time synchronous Averaging
Spectral Whitening
Filtering around fault frequencies
SPWVD for each carrier revolution
Compute the mean of all the SPWVD
Spectral Whitening
Benefits : modify the spectral characteristics of a signal to make it more "white" or evenly distributed across the frequency spectrum.
Randall, R. B. (2017). A history of cepstrum analysis and its application to mechanical problems. Mechanical Systems and Signal Processing, 97, 3-19.

## Slide 17: Improved time-frequency map
Vibration signal in time domain
Tachometer Signal
Resampling in angular domain
Time synchronous Averaging
Spectral Whitening
Filtering around fault frequencies
SPWVD for each carrier revolution
Compute the mean of all the SPWVD
Filtering around fault frequencies (Model)
Benefits :
- Sensitivity to only planet gears anisotropy.
- Sensitivity to incipient planet gears anisotropy.
Method :
- Set all other Fourier coefficients besides the fault frequencies to zero in the spectrum.
Feng, Z., & Zuo, M. J. (2012). Vibration signal models for fault diagnosis of planetary gearboxes. Journal of Sound and Vibration, 331(22), 4919-4939.
Fault on the planet gear :

## Slide 18: Improved time-frequency map
Vibration signal in time domain
Tachometer Signal
Resampling in angular domain
Time synchronous Averaging
Spectral Whitening
Filtering around fault frequencies
SPWVD for each carrier revolution
Compute the mean of all the SPWVD
Smoothed Pseudo Wigner-Ville Distribution
Tradeoff : Time-frequency resolution VS Cross-terms interference.
Flandrin, P. (2018). Explorations in time-frequency analysis. Cambridge University Press.
The SPWVD is a time-frequency representation that provides a detailed analysis of a signal's energy distribution in both time and frequency domains.
SPWVD uses independent windows to smooth Wigner-Ville Distribution in time and frequency.

## Slide 19: Improved time-frequency map
Vibration signal in time domain
Tachometer Signal
Resampling in angular domain
Time synchronous Averaging
Spectral Whitening
Filtering around fault frequencies
SPWVD for each carrier revolution
Compute the mean of all the SPWVD
The final map
Benefits : Attenuate noise and non-synchronous phenomenon.

## Slide 20: Experimental results
Simulation on Airbus Databases
Data : Vibration sensor mounted on the housing radially and one tachometer sensor on the planet carrier shaft
Algorithm configuration : Confidential !
For database N° 1:
  A planet gear fault, denoted anisotropy 1, appeared after a high torque regime.
For database N° 2:
  The indicator increases as soon as a healthy planet gear was replaced by a faulty one.
  The indicator decreases when we switch the planet gears again.
  The indicator increases again after initiating a planet gear fault through high load

## Slide 21: Conclusion
The Time Frequency Representation are
  Adapted to analyze non-stationary signals from real world complex application.
  Useful for developing health indicators for machine monitoring systems.
To overcome some time frequency representation problems :
  Choose the optimal TFR methods by taking into consideration the time frequency resolution, the interference / cross terms, and the computation cost.
  Use preprocessing techniques to optimize and enhance the time frequency maps.
Next steps :
  Use and Enhance the spectrogram maps (low computation time and complexity).
  Find new ways to compute robust indicators from TFRs.

## Slide 22
Thank you for your attention
LASPI UJM - Saint Etienne